## Slide 1: The International Standards for the Safety of Radioactive Waste Management
Japie van Blerk
AquiSim Consulting (Pty) Ltd, South Africa
aquisim@netactive.co.za
Sustaining Cradle-to-Grave Control of Radioactive Sources (INT-9182) Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017

## Slide 2: History
Statutory Obligation: Under Article III, Paragraph A.6 of the Statute (1957), the IAEA is required:
        “ To establish or adopt, in consultation and, where appropriate, in collaboration with the competent organs of the United Nations and with the specialized agencies concerned,
        standards of safety for protection of health and minimization of danger to life and property (including such standards for labour conditions), and
        to provide for the application of these standards to its own operation as well as to the operations making use of materials, services, equipment, facilities, and information made available by the Agency …;
  In 1958, the IAEA published its first Safety Standard, Safety Series No. 1, Safety Handling of Radioisotopes

## Slide 3: History
Over the year, the IAEA published all kinds of documents related to safety (more than 200 in the Safety Series):
  fundamentals (silver)
  standards (red)
  guides (green)
  reports (brown/purple)
  practices (blue)

## Slide 4: Development of Safety Standards
Objective is to have consensus at the highest level
  Commission on Safety Standards and the Committees were established with the objective of achieving consensus, quality, coherence and consistency in the development of international standards for safety
                IAEA safety standards are developed in close consultation with Member States and with representatives of relevant international organizations
                Approval by the Board of Governors is required for Safety Fundamentals and Safety Requirements.
                The authority to establish Safety Guides has been delegated to the IAEA Director General

## Slide 5
Development of Safety Standards
Outline and work plan
Prepared by the Secretariat
Review by the Safety Standards Committees
and the Commission on Safety Standards
Drafting or revising
of safety standard
by the Secretariat and Consultants
Review
by the Safety Standards
Committee(s)
Endorsement
by Commission on Safety Standards
Member
States
Approval by the IAEA’s
Director General or BoG *
MS involved
* SF and SRs approved by BoG
* SGs approved by DG
Review period:
about every 5 years
Draft
Final Draft
Draft
Comments
Notes: Clear categories of safety standards consistent with Member States’ needs and use
Clear, logical and integrated structure based on a unified philosophy of safety
Consensus at the highest level on what constitutes a high level of safety and the related best international practices
Transparency and rigour of the process
Effective feedback mechanisms
Developed and reviewed by IAEA staff and international experts
With close consultation with Member States
All IAEA Member States may nominate experts for the safety standards committees and may provide comments on draft standards
Interaction with other international organizations – UNSCEAR, ICRP, WHO, FAO, UNEP, OECD NEA
SF and SRs approved by the Board of Governors
SGs are approved by IAEA DG
Review periodicity is about 10 years
Since 1996 more than 100 volumes published
Review
About every 5 years
Revision of DPPs
Following the process of standards' development (Committees, CSS, BOG, etc)

## Slide 6: Safety Standards Hierarchy & Categories
The structure of the safety standards reflects the ten Fundamental Safety Principles and the “Roadmap” on the long-term structure of the safety standards
Requirements address what shall be done
General Safety Requirements: Applicable to all facilities and activities
Specific Safety Requirements: Applicable to specified facilities or activities
Expressed as “shall” statements
Provide guidance on how to implement safety requirements or how the requirements may be achieved
General or Specific Safety Guides
Expressed as “should” statements

## Slide 7
Structure of the Safety Standards
Notes: Clear Logical and Integrated Structure. Some of these are finalized, while others are in a process of being drafted or are in a review process

## Slide 8: Other IAEA Publications
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 9: Status of Safety Standards
IAEA Safety standards are
  Binding for IAEA’s own activities
  Not binding on the Member States
BUT
  may be adopted by them and directly used as reference for review of national standards and as benchmark for harmonization
EXCEPT
  In relation to operations assisted by the IAEA e.g.:
    Integrated Regulatory Review Service
    Technical Cooperation Fund work
    States wishing to enter into project agreements with the IAEA
http://www-ns.iaea.org/standards/default.asp
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 10: Status of Safety Standards
Drafters of safety and security related IAEA publications — particularly safety standards — should use terms as recommended by the IAEA Safety Glossary
No individual glossary in individual publications.
If a need to add or revise a definition of the IAEA Safety Glossary is identified through the development or revision of a safety standard, the proposal will be submitted to the review process and to the meeting of the four Chairs and if agreed, the Safety Glossary will be updated accordingly

## Slide 11: Status of Safety Standards
Safety Standards reflect a consensus at the highest level on what constitutes a high level of safety
The Standards can be used to draft and to review the national reports in the framework of the Convention on Nuclear Safety (CNS) and the Joint Convention on the safety of spent fuel management and on the safety of radioactive waste management (JC)
The Standards are the basis for the Integrated Regulatory Review Service (IRRS)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 12
Structure of the Safety Standards
Notes: Clear Logical and Integrated Structure. Some of these are finalized, while others are in a process of being drafted or are in a review process

## Slide 13: Safety Fundamentals
The fundamental safety objective is to protect people - individually and collectively - and the environment from harmful effects of radiation (without unduly limiting the operation of facilities or the conduct of activities that give rise to radiation risks)
To achieve the highest standards of safety that can reasonably be achieved, measures have to be taken:
  to control the radiation exposure of people
  to control the release of radioactive material to the environment
  to restrict the likelihood of events that may lead to loss of control of a source of radiation
  to mitigate the consequences of such events if they were to occur
Policy document of the IAEA Safety Standards Series:
States the basic objectives, concepts and principles involved in ensuring protection and safety
          1 Objective
          10 safety principles
Notes: 13

## Slide 14: Safety Fundamentals
Responsibility for safety
Role of government
Leadership and management for safety
Justification of facilities and activities
Optimization of protection
Limitation of risks to individuals
Protection of present and future generations
People and the environment, present and future, must be protected against radiation risks
Prevention of accidents
Emergency preparedness and response
Protective actions to reduce existing or unregulated radiation risks
Policy document of the IAEA Safety Standards Series:
States the basic objectives, concepts and principles involved in ensuring protection and safety
          1 Objective
          10 safety principles
Notes: 14

## Slide 15
Structure of the Safety Standards
Notes: Clear Logical and Integrated Structure. Some of these are finalized, while others are in a process of being drafted or are in a review process

## Slide 16: General Safety Requirements
GSR Part 1 Governmental Legal and Regulatory Framework for Safety
  Covers all phases of the lifetime of facilities and activities, from the use of a limited number of radiation sources to a nuclear power programme, until release from regulatory control
  Covers 3 major areas with 36 requirements
    Responsibilities and Functions of the Government (13)
    The Global Safety Regime (2)
    Responsibilities and Functions of Regulatory Body

## Slide 17: General Safety Requirements
GSR Part 1 Responsibilities and Functions of the Government
  National policy and strategy for safety
  Establishment of a framework for safety
  Establishment of an independent regulatory body
  Prime responsibility for safety
GSR Part 1 - Global Safety Regime
  International obligations and arrangements for international cooperation
  Sharing of operating experience and regulatory experience
GSR Part 1 - Responsibilities and Functions of the Regulatory Body
  Organization; resources; staffing; competence; management
  Independence in the performance of regulatory functions
  Management of adequate records relating to safety
  Stability and consistency of regulatory control
  Regulatory functions, etc.
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 18: General Safety Requirements
GSR Part 2 Leadership and Management for Safety (to replace GS-R-3)
  To define requirements for establishing, implementing, assessing and continually improving a management system that integrates safety, health, environmental, security, quality and economic elements to ensure that safety is properly taken into account in all the activities of an organization
  To ensure, by considering the implications of all actions not within separate management systems but with regard to safety as a whole, that safety is not compromised
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 19: General Safety Requirements
GS-R-3 Management Systems: General requirements for the management system, including those relating to safety culture, grading and documentation
GS-R-3 Management responsibility: Responsibilities of senior management for the development and implementation of a management system
GS-R-3 Resource management
GS-R-3 Process implementation: Processes of the organization specification, development and management, including the generic processes of the management system
GS-R-3 Measurement, assessment and improvement: Measuring, assessing and improving the management system
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 20: General Safety Requirements
GSR Part 3 Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards
This publication establishes requirements for the protection of people and the environment from harmful effects of ionizing radiation and for the safety of radiation sources
Replaced the Basic Safety Standards of 1996
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 21: General Safety Requirements
GSR Part 3 Radiation Protection and Safety of Radiation Sources: International Basic Safety Standards
General Requirements for Protection and Safety
  Responsibilities of government, regulator, operators
  Management requirements
Planned Exposure Situations
  Public exposure
  Medical exposure
  Occupational exposure.
Emergency Exposure Situations
  Public and worker exposure
  Transition from emergency to existing exposure situation
Existing Exposure Situation
  Public and worker exposure
Exemption Levels, Dose Conversion Factors
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 22: General Safety Requirements
GSR Part 4 Safety Assessment for Facilities and Activities
This publication establishes the generally applicable requirements to be fulfilled in safety assessment for facilities and activities
  Defence in depth, quantitative analyses and the application of a graded approach to the ranges of facilities and of activities that are addressed
  Independent verification of the safety assessment that needs to be carried out by the originators and users of the safety assessment
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 23: General Safety Requirements
GSR Part 4 Safety Assessment for Facilities and Activities
Basis for Requiring a Safety Assessment
  Basis for requiring a safety assessment to be carried out, derived from SF-1
Graded Approach
  to implementation of the requirements for safety assessment for different facilities and activities.
Safety Assessment
  Overall requirements for a safety assessment and specific requirements that relate to the assessment of features relevant to safety
  Requirements to address: defence in depth and safety margins, to perform safety analysis, to document the safety assessment and to carry out an independent verification
Management and Maintenance of the Safety Assessment
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 24: General Safety Requirements
GSR Part 5 Pre-Disposal of Radioactive Waste
OBJECTIVES
To establish the requirements that must be satisfied in the predisposal management of RW
To sets out the objectives, criteria and requirements that apply to all stage of predisposal management facilities
SCOPE
Predisposal management of all types of RW
Predisposal management from generation up to disposal (incl. processing, storage, transport)
Do not repeat requirements in other Safety Requirements
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 25: General Safety Requirements
GSR Part 5 Pre-Disposal of Radioactive Waste
  This publication establishes the requirements that must be satisfied in the predisposal management of radioactive waste
  It sets out the objectives, criteria and requirements for the protection of human health and the environment that apply to the siting, design, construction, commissioning, operation and shutdown of facilities for the predisposal management of radioactive waste, and the requirements that must be met to ensure the safety of such facilities and activities
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 26
RESPONSIBILITIES ASSOCIATED WITH THE PREDISPOSAL MANAGEMENT OF RADIOACTIVE WASTE
General
Legal, regulatory and policy framework
Requirement 1: Legal and regulatory framework
Requirement 2: National policy and strategy on radioactive waste management
Requirement 3: Responsibilities of the regulatory body
Operators
Requirement 4: Responsibilities of the operator
Integrated approach to safety
Requirement 5: Requirements in respect of security measures
Requirement 6: Interdependences
Requirement 7: Management systems
STEPS IN THE PREDISPOSAL MANAGEMENT OF RADIOACTIVE WASTE
Generation of radioactive waste
Requirement 8: Radioactive waste generation and control
Requirement 9: Characterization and classification of radioactive waste
Processing of radioactive waste
Requirement 10: Processing of radioactive waste
Storage of radioactive waste
Requirement 11: Storage of radioactive waste
Radioactive waste acceptance criteria
Requirement 12: Radioactive waste acceptance criteria
General Safety Requirements

## Slide 27: General Safety Requirements
DEVELOPMENT AND OPERATION OF PREDISPOSAL RADIOACTIVE WASTE MANAGEMENT FACILITIES AND ACTIVITIES
General
Approach to safety
Requirement 13: Preparation of the safety case and supporting safety assessment
Requirement 14: Scope of the safety case and supporting safety assessment
Requirement 15: Documentation of the safety case and supporting safety assessment
Requirement 16: Periodic safety reviews
Development of predisposal radioactive waste management facilities
Requirement 17: Location and design of facilities
Requirement 18: Construction and commissioning of the facilities
Requirement 19: Facility operation
Requirement 20: Shutdown and decommissioning of facilities
Other provisions
Requirement 21: System of accounting for and control of nuclear material
Requirement 22: Existing facilities

## Slide 28: General Safety Requirements
GSR Part 6 Decommissioning of Facilities
  This publication establishes the general safety requirements to be met during planning for decommissioning, during conduct of decommissioning actions and during termination of authorization for decommissioning
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 29: General Safety Requirements
GSR Part 7 Preparedness and Response for a Nuclear or Radiological Emergency
  This publication establishes the requirements for an adequate level of preparedness and response for a nuclear or radiological emergency in any State
  These requirements are intended to be applied by authorities at the national level by means of adopting legislation, establishing regulations and assigning responsibilities will replace
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 30
Structure of the Safety Standards
Notes: Clear Logical and Integrated Structure. Some of these are finalized, while others are in a process of being drafted or are in a review process

## Slide 31: Specific Safety Requirement
SSR-1
SSR-2
SSR-3
SSR-4
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 32: Specific Safety Requirement
SSR-5 Disposal of Radioactive Waste
  This publication sets out the safety objective and criteria for the disposal of all types of radioactive waste and establishes the requirements that must be satisfied in the disposal of radioactive waste.
  This publication is intended for use by all persons responsible for, and concerned with, radioactive waste management and making decisions in relation to the development, operation and closure of disposal facilities, especially those persons concerned with the related regulatory aspects
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 33: Specific Safety Requirement
Applicable to disposal of all types of waste in designed disposal facilities
Covers
Operational phase
Post-closure phase
Does not address
  Broader issues of site selection
  Transportation of waste to the site
  Non radiological environmental impact
Stakeholder involvement important, but beyond the scope of the standard
Consistent with ICRP Publications 77, 81 and 103
A total of 26 requirements

## Slide 34: Specific Safety Requirement (SSR-5)
REQUIREMENTS FOR PLANNING DISPOSAL FACILITIES
  LEGAL AND ORGANIZATIONAL FRAMEWORK
  SAFETY APPROACH
  SAFETY DESIGN PRINCIPLES
REQUIREMENTS FOR THE DEVELOPMENT, OPERATION AND CLOSURE OF DISPOSAL FACILITIES
  FRAMEWORK FOR DISPOSAL
  THE SAFETY CASE AND SAFETY ASSESSMENT
  STEPS IN THE DEVELOPMENT, OPERATION AND CLOSURE OF DISPOSAL FACILITIES
REQUIREMENTS FOR ASSURANCE OF SAFETY
EXISTING DISPOSAL FACILITIES
IRPA14 – Cape Town, 9-13 May 2016

## Slide 35: Specific Safety Requirement (SSR-5)
Government responsibility
Regulator’s responsibility
Operator’s responsibility
Safety in development and operation
Passive means for safety
Understanding and confidence in safety
Multiple safety functions
Containment
Isolation
Surveillance and control
Stepwise development
Using the safety case
Scope of the safety case
Documenting the safety case
Site characterization
Design
Construction
Operation
Closure
Waste acceptance
Monitoring
Post-closure & institutional control
Accountancy and control
Nuclear security measures
Management systems
Existing disposal facilities

## Slide 36: Specific Safety Requirement
SSR-6 Regulations for the Safe Transport of Radioactive Material 2012 Edition
  This publication establishes requirements that must be satisfied to ensure safety and to protect persons, property and the environment from the effects of radiation in the transport of radioactive material.
  This protection is achieved by requiring:
    Containment of the radioactive contents;
    Control of external radiation levels;
    Prevention of criticality; and
    Prevention of damage caused by heat
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 37
Structure of the Safety Standards
Notes: Clear Logical and Integrated Structure. Some of these are finalized, while others are in a process of being drafted or are in a review process

## Slide 38: Safety Guides for Safety Requirements
GSR Part 1, Governmental, Legal and Regulatory Framework for Safety (2010)
GS-G-1.1, Organization and Staffing of the Regulatory Body for Nuclear Facilities (2002)
GS-G-1.2, Review and Assessment of Nuclear Facilities by the Regulatory Body (2002)
GS-G-1.3, Regulatory Inspection of Nuclear Facilities and Enforcement by the Regulatory Body (2002)
GS-G-1.4, Documentation for Use in Regulating Nuclear Facilities (2002)
GS-G-1.5, Regulatory Control of Radiation Sources (2004)
GSG-4, Use of External Experts by the Regulatory Body (2013)
SSG-12, Licensing Process for Nuclear Installations (2010)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 39: Safety Guides for Safety Requirements
The Management System for Facilities and Activities (2006)
GS-G-3.1, Application of the Management System for Facilities and Activities (2006)
GS-G-3.3, The Management System for the Processing, Handling and Storage of Radioactive Waste (2008)
GS-G-3.4, The Management System for the Disposal of Radioactive Waste (2008)
GS-G-3.5, The Management System for Nuclear Installations (2008)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 40: Safety Guides for Safety Requirements
GSR Part 3, Radiation Protection and Safety of Radiation Sources (2014)
RS-G-1.7, Application of the Concepts of Exclusion, Exemption and Clearance (2004)
RS-G-1.8, Environmental and Source Monitoring for Purposes of Radiation Protection (2005)
SSG-17, Control of Orphan Sources and Other Radioactive Material in the Metal Recycling and Production Industries (2012)
RS-G-1.10, Safety of Radiation Generators and Sealed Radioactive Sources (2006)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 41: Safety Guides for Safety Requirements
GSR Part 4, Safety Assessment for Facilities and Activities (2009)
WS-G-5.2, Safety Assessment for the Decommissioning of Facilities Using Radioactive Material (2009)
GSG-3, The Safety Case and Safety Assessment for the Predisposal of Radioactive Waste (2013)
SSG-23, The Safety Case and Safety Assessment for the Disposal of Radioactive Waste (2012)
SSG-15, Storage of Spent Nuclear Fuel (2012)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 42: Safety Guides for Safety Requirements
GSR Part 5, Predisposal Management of Radioactive Waste (May 2009)
WS-G-1.2, Management of Radioactive Waste from the Mining and Milling of Ores (2002)
WS-G-2.3, Regulatory Control of Radioactive Discharges to the Environment (2000)
WS-G-2.5, Predisposal Management of Low and Intermediate Level Radioactive Waste (2003)
WS-G-2.6, Predisposal Management of High Level Radioactive Waste (2003)
WS-G-2.7, Management of Waste from the Use of Radioactive Material in Medicine, Industry, Agriculture, Research and Education (2005)
WS-G-6.1, Storage of Radioactive Waste (2006)
GSG-1, Classification of Radioactive Waste (2009)
GSG-3, The Safety Case and Safety Assessment for the Predisposal of Radioactive Waste (2013)
SSG-15, Storage of Spent Nuclear Fuel (2012)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 43: Safety Guides for Safety Requirements
GSR Part 6, Decommissioning of Facilities (2014)
WS-G-2.1, Decommissioning of Nuclear Power Plants and Research Reactors (1999)
WS-G-2.2, Decommissioning of Medical, Industrial and Research Facilities (1999)
WS-G-2.4, Decommissioning of Nuclear Fuel Cycle Facilities (2001)
WS-G-3.1, Remediation Process for Areas Affected by Past Activities and Accidents (2007)
WS-G-5.1, Release of Sites from Regulatory Control upon Termination of Practices (2006)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 44: Safety Guides for Safety Requirements
GS-R-2, Preparedness and Response for a Nuclear or Radiological Emergency (2002)
GS-G-2.1, Arrangements for Preparedness for a Nuclear or Radiological Emergency (2007)
GSG-2, Criteria for Use in Preparedness and Response for a Nuclear or Radiological Emergency (2011)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 45: Safety Guides for Safety Requirements
NS-R-3, Site Evaluation for Nuclear Installations (2003)
SSG-9, Seismic Hazards in Site Evaluation for Nuclear Installations (2010)
SSG-18, Meteorological and Hydrological Hazards in Site Evaluation for Nuclear Installations (2011)
SSG-21, Volcanic Hazards in Site Evaluation for Nuclear Installations (2012)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 46: Safety Guides for Safety Requirements
SSR-2/1, Safety of Nuclear Power Plants: Design (2012)
NS-G-1.13, Radiation Protection Aspects of Design for Nuclear Power Plants (2005)
SSR-2/2, Safety of Nuclear Power Plants: Commissioning and Operation ( 2011)
NS-G-2.7, Radiation Protection and Radioactive Waste Management in the Operation of Nuclear Power Plants (2002)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 47: Safety Guides for Safety Requirements
NS-R-4, Safety of Research Reactors (2005)
NS-G-4.6, Radiation Protection and Radioactive Waste Management in the Design and Operation of Research Reactors (2009)
NS-R-5 (Rev 1), Safety of Nuclear Fuel Cycle Facilities (May 2014)
SSG-5, Safety of Conversion Facilities and Uranium Enrichment Facilities (2010)
SSG-6, Safety of Uranium Fuel Fabrication Facilities (2010)
SSG-7, Safety of Uranium and Plutonium Mixed Oxide Fuel Fabrication Facilities (2010)
SSG-15, Storage of Spent Nuclear Fuel (2012)
SSG-27, Criticality Safety in the Handling of Fissile Material (2014)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 48: Safety Guides for Safety Requirements
SSR-5, Disposal of Radioactive Waste (2011)
SSG-1, Borehole Disposal Facilities of Radioactive Waste (2006)
SSG-14, Geological Disposal Facilities for Radioactive Waste (2011)
SSG-23, The Safety Case and Safety Assessment for the Disposal of Radioactive Waste (2012)
SSG-29, Near Surface Disposal Facilities for Radioactive Waste (2014)
SSG-31, Monitoring and Surveillance of Radioactive Waste Disposal Facilities (2014)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 49: Safety Guides for Safety Requirements
SSR-6, Regulations for the Safe Transport of Radioactive Material, 2012 edition (2012)
TS-G-1.1, Advisory Material for the IAEA Regulations for the Safe Transport of Radioactive Material (2008)
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 50
Safety Standards: Management of DSRS

## Slide 51
Safety Standards: Management of DSRS

## Slide 52
Safety Standards: Management of DSRS
DS 477
Revision
DS 454
Revision

## Slide 53: Summary
Safety Standards = Safety Fundamentals + Safety Requirements + Safety Guides
10 fundamental principles (SF-1) are the basis for the development of requirements and guides
General Safety Requirements apply to all facilities and activities
Specific Safety Requirements…
Collection of general and specific Safety Guides reflect a consensus on what constitutes a high level of safety
Notes: An integrated, comprehensive and consistent set of up-to-date, user friendly and fit-for-purpose IAEA safety standards of a high quality.
Using and applying the IAEA safety standards will provide for a world wide harmonized high level protection for people and the environment from harmful effects of ionizing radiation.

## Slide 54
Thank you!