## Slide 1: Sustaining Cradle-to-Grave Control of Radioactive Sources (INT-9182) Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017
Professors. Rehab Abdel Rahman and Ahmed Zaki
Hot laboratory and waste management centre, Egypt
Status of Safety Assessment for Egyptian Waste Management Facilities for DSRS (Storage and Disposal Facilities)

## Slide 2
Cairo
Inshas
Inshas comlex is located at about 50 km north-east of Cairo city .
It is fixed by longitudes 31° 24' and latitude 30° 17'.
The site is bounded from the west by the Ismailia canal and the desert in east.
Location of Inshas storages and Disposal Facilities
Arab Republic of Egypt
Red Sea
Mediterranean Sea
Sinai
Western Desert
Eastern
Desert
The Sudan
L
I
B
Y
A

## Slide 3: Radioactive Waste Generation in Egypt
Inshas complex
2MW Research Reactor
22 MW Research Reactor
Radioisotope production lab.
Gamma irradiator
Nuclear fuel production lab.
Decontamination activities
Other External Generators
Medical uses: Hospital, medical lab.
Research uses: Research institute, universities
Industrial uses: Petroleum, inspection , etc.
NORM

## Slide 4
Inventory of DSRS

## Slide 5: Types and categories of the Different DRSS in Egypt

## Slide 6: Categories of DSRS

## Slide 7: National Waste Management Facilities for DSRS (Stores)
Stores
  Two types of centralized storage facility i.e. old (hanger) and new (concrete)
  Location: Atomic Energy Authority of Egypt campus in Inshas, Cairo.
  Purpose: Store safely the waste this includes sealed sources (conditioned & unconditioned) and conditioned radioactive wastes

## Slide 8: National Waste Management Facilities for DSRS
  Stage of development:
  stores are in operational phase
  Safety functions:
  Confinement of radioactive material,
  shielding against radiation
  Control of planned radioactive releases,
  Limit accidental releases.

## Slide 9: Status of Safety Case / Safety Assessment for DSRS Stores
For each existing or planned store, is there a Safety Case / Safety Assessment (SC/SA)?
  Yes, draft for safety case for sealed sources stores only were developed
Is the SC/SA draft or final?
  Three versions of SC draft
How was the SC/SA reviewed?
  Beer review was performed by operator, and independent reviewer
  Sc is not finally approved
Where are the documents kept?
  Copies of the drafts are distributed at the operator

## Slide 10: Status of Safety Case / Safety Assessment for DSRS Stores
What is the scope and contents of the SC/SA for the store(s)?
  SC cover operation- decommissioning phases are addressed
  The following issues are addressed
    Management system,
    Operating procedures,
    Radiation protection plans,
    Monitoring arrangements,
    Emergency plans, and
    Safety assessment

## Slide 11: Status of Safety Case / Safety Assessment for DSRS Stores
In more detail, what does the safety assessment cover?
  Occupational and public exposures for normal operational exposure (due to reduced efficiency of the filtration system )
  Occupational and public exposure due to accidents and emergency situations(Drop incident )

## Slide 12: Status of Safety Case / Safety Assessment for DSRS Stores
In more detail, what does the safety assessment cover?
  How are exposure scenarios identified, described and assessed?
    Scenarios were identified based on the operational procedure and available FEP in SAFRAN.
    Safety of transport scenario, were included then was eliminated based on reviewers recommendations.
    Exposure scenario were quantitatively and qualitatively assessed
  How are exposures quantified (modelled)?
    Using safran
  How are the assessment results used?
    To identify store capacity
    to manage worker doses

## Slide 13: Inshas disposal Facility
Selection of the repository site was carried out between 1999 and 2007.
Out of 10 sites selected on preliminary basis, 3 were chosen for further investigation and based on agreed site selection criteria,
The Inshas site was chosen as the most suitable site

## Slide 14: Near surface disposal facility at Inshas site
The final step of the national LILW management system is disposal in a near surface disposal facility at Inshas site.
Its safety is ensured by combination of engineered and natural barriers that keep the disposal vaults dry and prevent radioactive releases into the environment.
The repository was built in geological formation with low permeability and high sorption capacity, and the disposal vaults were surrounded by an additional artificial construction clay layer.

## Slide 15
4 cuboid modules of 10 m
length x5 m width x 3m
depth each.
Collecting
well

## Slide 16
Notes: There is an administration and control building
Operational (temporary cover) is used
4 modules of 10mx5mx3m depth

## Slide 17
Inshas near surface disposal facility
Permission for construction and temporary operation for low surface dose rate package was granted by the regulatory body according to this permission about 100 containers were disposed of.
Notes: 1m-3 enforced concrete waste package is used
A well for collecting the infiltration water to be assed and treated

## Slide 18
A cross section of the proposed cover of Inshas disposal facility
5 barrier layers
6 Engineering barriers are used for Inshas Disposal Facility
Notes: In addition to the waste package, backfill , immobilization cement matrix , 6 engineering barriers are used for Inshas Disposal Facility

## Slide 19
Hydrology and Geology of Inshas site

## Slide 20: Schematic presentation of ground water flow system at Inshas site
The Miocene aquifer is of a confined to semi-confined with piezometric head that amounts to three atmospheric pressure, the static water level is recorded at about 13 to 14 m from ground surface
Notes: Miocene aquifer is 38 m from ground surface
The absolute level of the groundwater is usually 13 to 13.5 m above the sea level
static water level is recorded at 10 m from ground surface

## Slide 21: Status of Safety Case / Safety Assessment for DSRS disposal Facility
  SA covers design , construction, operation and post closure, not include decommissioning
  SA address the management system, operating procedures
  There is a general emergency plan, the disposal facility is part of it

## Slide 22: Status of Safety Case / Safety Assessment for DSRS disposal Facility
There is a Safety Assessment achieved by the operator (HLWMC) ,reviewed and approved by the regulator body
The documents are kept at regulator body
SA covers the operational and post closure scenarios of the facility.

## Slide 23
PAGAN (Performance Assessment Ground-water Analysis of low-level Nuclear waste) is used to study the safety assessment of Inshas disposal site.
The main exposure path way adopted in the analysis is the ground-water to the man. Assuming a 70-kg weight man drinks two liters of ground-water from a well located 150 m distance a way from Inshas disposal site
The assumptions and the parameters used in the analysis depend on the :
1-Inshas site characteristics
2-the type of waste arising from the research, development and that arise from industry and hospitals (Cs-137, Sr-90, and Co-60)
Assumption and scenarios

## Slide 24
Assumption and scenarios
3-The design of the disposal site
4-The hydrology and the geohydrology of the site and the type of Inshas soils Kd values.
5-The worst case ; there is no unsaturated zone.
6-The engineering barrier is completely failed (no engineering barrier exists)
7-The Well Scenario (a well located 150 m)
8-River Scenario (Ismailia Canal)

## Slide 25
TSD-DOSE was used to estimate potential doses to :
(1) The driver at the landfill, resulting from external irradiation
(2) The waste-placement operator, resulting from external irradiation
and inhalation of contaminated particulate; and
(3) The general public, resulting from inhalation of contaminated particulate, external irradiation, incidental ingestion of contaminated particulate, and ingestion of contaminated foodstuff.
For the worker scenarios, exposure times were based on the volume of waste to be” disposed of.
External doses were modeled at a distance of 0.6 m from the source for the driver For the waste-placement operator, a distance of 1.5 m was assumed for inspection activities and a distance of 3 m was assumed for disposal activities.
Operational safety assessment scenarios (Disposal)

## Slide 26: Borehole Disposal
Egypt is adopting borehole disposal concept to permanently isolate the unused sealed sources from biosphere , specially that of half lives greater than 30 years such as Am-241 and high active SHARS sources
Both concepts of South Africa (Borehole for Sealed Sources; BOSS) and USA (Greater Confinement Disposal; GCD) are under studies to adopt one of them to be implemented.
The option selected for a particular sealed source will depend on the variety of relevant factors including activity, radioisotopes content, terms of the purchasing contract and physical condition of the source.

## Slide 27: Borehole Disposal of Sealed Disused Sources (BOSS) Versus GCD

## Slide 28: Conclusions
A lot of work is needed to achieve the SA and SC of Inshas near surface facility
May the facility be assumed to be a long term storage (50 years) or a disposal for DSRS and LLW &ILW?
Choice of a borehole disposal concept (which one; BOSS or GCD) is suitable for Egyptian case.
Are we have to look for sites rather than Inshas for borehole disposal?

## Slide 29: Thank you!
Notes: Thank you!