## Slide 1: Sustaining Cradle-to-Grave Control of Radioactive Sources (INT-9182) Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017
Status of Safety Cases and Safety Assessments for National Waste Management Facilities for DSRS
in ETHIOPIA

## Slide 2: National Waste Management Facilities for DSRS
Disused Radioactive sealed Source (DSRS) in Ethiopia
ERPA has Established and organized a dedicated central storage facility .
DSRS are collected and managed in the dedicated newly built radioactive waste management facility, which is operational since 2014.
During the design and construction of this facility several aspects like radiation protections, security, structural adequacy, environmental impact assessment were considered.
The Design, construction and operation provide and maintain several levels of protection to limit possible radiological impacts.
Appropriate physical protection ( deference in depth) and security systems have been established

## Slide 3: National Waste Management Facilities for DSRS
DSRS in Ethiopia
The Radioactive Waste Management facility is authorized to operate, collect, transport, segregate, treatment, conditioning and storage of DSRS in Ethiopia.
Some disused sealed sources are conditioned by several technologies, such as cementation, encapsulation, and over-packages.
In principle Ethiopia imports Radioactive sources , and at the end of life time export to the manufacturer/supplier
safety assessments at the DSRS storage facility at interim storage facility has been established and appropriately implemented to ensure safe and secure management of DSRS following graded approach
Getting information, data, resources
Safety provisions
monitoring of the facility and its environment(occupational exposure, public exposure, normal operational exposure situation, any exposure path way
full documentation of wastes stored (inventory)
properly trained operators and others

## Slide 5: The new Radioactive waste Management Facility with Appropriate physical protection and security systems.

## Slide 7
RAS Collected for Conditioning from Different Users

## Slide 8
the previous ERPA Radioactive Waste Interim Storage

## Slide 9: NATIONAL WASTE INVENTORY
The record keeping and inventory of DSRS has been developed, and the national inventory of stored DSRS has been made up to date.
There are conditioned radioactive sources of 63 mCi, Radium 226; 1.59 GBq, Cs-137, Co-60 & Sr-90; 0.56 GBq Am-241, unconditioned RASs of:2.5kCi Co-60 (date ?), Am-241 unknown activity, 870 Ci C0-60 (22/05/09), and many LL sources – like check sources are kept at the interim storage of ERPA.

## Slide 10: Radioactive waste inventory Short Half Life Radioactive Sources ( solid)
I No. | II Radionuclide | III Activity (Year, D. of M. Unknown) | IV Quantity in TBq
1 | P-32 | 37 MBq | 3.70E-05
2 | S-35 | 1mCi | 1.00E-05
3 | Sterile generator | 6.38 GBq | 6.38E-03
4 | I131 | 370 GBq | 3.70E-01
5 | I131 | 370 GBq | 3.70E-01

## Slide 11: Inventory of the conditioned radioactive waste
I Package No. | II Shield No. | III Capsule No | IV Radionuclides | V Acvtivity - Year (GBq-2002) | VI D-value TBq | VII Ratio of A/D | VIII Category A/D based | IX No, of sources
ETH 01 | S1 | 1 | Ra-226 | 1.46 (43mg) | 4.00E-02 | 3.65E-02 | 4 | 9
 |  | 3 | Ra-226 | 0.9 (24 mg) | 4.00E-02 | 2.25E-02 | 4 | 2
ETH 02 | S2 | 1 | Cs-137 | 7.40E-01 | 1.00E-01 | 7.40E-03 | 5 | 3
 |  | 2 | Co-60 | 1.10E-01 | 3.00E-02 | 3.67E-03 | 5 | 1
 |  | 4 | Sr-90- | 7.40E-01 | 4.00E+00 | 1.85E-04 | 5 | 1
ETH 03 | S3 | ETH/02241 | Am-241 | 5.90E-01 | 6.00E-02 | 9.83E-03 | 5 | 1

## Slide 12: Inventory of the unconditioned spent/disused radioactive waste
No. | Radionuclide | III Activity | IV Remark
1 | Am-241 | 3 Ci | Needs to be conditioned
2 | Co-60 | 2.5 kCi | Irradiator
3 | Unknown (but tried to be identified as Am-241) | Unknown | Orphan Source Recovered (Metal Shielded)
4 | Unknown | Unknown | 25 (calibration sources for well logging?)
5 | Co-60 | 868 Ci (May 22, 2009 | Spent Teletherapy Source
6 | Cs-137 | 3.7 GBq | disused density gauge Midroc
7 | Cs-137 | 11.1GBq | disused density gauge Midroc
8 | Ir192 | 100Ci | Irradiator (Used) EAL
9 | Ir192 | Un known | Search and secure( Russian made)
10 | Co-60 | 0.015Ci | Irradiator(used) EAL
11 | Am-241/Be | 1.85 GBq | disused moisture density gauge
 | Cs-137 | 0.370 GBq | 
12 | Am-241/Be | 1.85 GBq | disused moisture density gauge

## Slide 13: Inventory of the unconditioned spent/disused radioactive waste
13 | Unknown (but tried to be identified as Pu 239 & Cs-137 | Unknown | Recovered Speed gauges from property collecting and Re-using Station scrap metal
14 | Unknown (but tried to be identified as Cs-135 | Unknown | Heavy army devices and gears from property collecting and Re-using Station
15 | Co-60 | 5 mCi | large metal sheet imported with machinery
16 | Cs-137 | 1.7477, 1.7169, 1.1322, 1.359, 1.702, 1.1174, 1.6983, 1.1248, 17353 GBq | Brachatherapy sources collected from Black lion hospital one set

## Slide 14: National Waste Management Facilities for DSRS
  NATIONAL Law/ POLICY/safety case FOR RAWM
  The existing law (RP Law 571/2008) does not have enough provisions for RAW management.
  A new legislation which is very comprehensive and consistent with the IAEA safety standards has been approved by the Councils of Ministers and forwarded to Parliament for final endorsement.
  The newly developed draft law comprises nuclear and radiation, safety,, security and safeguards issues.
  Legal aspect for detail RAWM is also included in a concise manner in the draft legislation
  The draft legislation specifies that the regulatory control is conducted by ERPA and operational aspects are handled by ERPA with the users having the primary responsibility
  At present Ethiopia has no national policy and strategy on RWM and a new draft RAWM Policy has been developed to be approved.
  ERPA requested expert mission from IAEA to help us to draft the national policy and strategy and In 2016, the expert mission on “Drafting the national policy and strategy for managing radioactive waste was held in Addis Ababa.
  No safety case document has been developed to date and to be considered.

## Slide 15: National Waste Management Facilities for DSRS
DSRS Disposal Facilities
Currently, there is no disposal facility/ repository in Ethiopia
Considerations may be make for the future waste management programs

## Slide 16: Thank you!
Notes: Thank you!