## Slide 1: Management
Paul Essel
Ghana Atomic Energy Commission
&
Henry Lawluvi
Nuclear Regulatory Authority-Ghana
Status of Safety Cases and Safety Assessments for National Waste Management Facilities for DSRS in Ghana
Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017

## Slide 2: Outline
Introduction
Regulatory Framework
National Waste Management Facilities for DSRS- Store
Status of Safety Case / Safety Assessment for DSRS-Stores
National Waste Management Facilities for DSRS-Disposal Facility
Status of SC/SA for DSRS-Disposal Facilities

## Slide 3
Sealed Radioactive Sources are being used in the following sectors in Ghana;
    Medical,
    Industry,
    Agriculture
    Research and teaching
    Others
The Disused Sealed Radioactive
Sources arising must be safely
managed
Introduction

## Slide 4: Introduction (2)
Ghana Atomic Energy Commission (GAEC) was established by an Act of Parliament (Act 204) in 1963 which has been superseded by Act 588 in 2000.
The GAEC is under the Ministry of Environment, Science, Technology and Innovation
The main functions of the Commission include the promotion and development of peaceful application of nuclear and biotechnology techniques for the benefit of Ghana.
In pursuance of the above objective GAEC has seven institutes which carry out the above mentioned functions.

## Slide 5: Legal and Regulatory Regime in Ghana (1)
From 1993 to 2015 the GAEC carried out regulatory functions through the Radiation Protection Board under the LI 1559 of 1993.
The Nuclear Regulatory Authority Act, 2015, Act 895, established the Nuclear Regulatory Authority (NRA) in Jan 2016
The NRA is the statutory regulatory authority in Ghana that regulates all practices involving radiation and radioactive sources from cradle to grave.
.
Regulatory Framework

## Slide 6: Central Waste Processing and Storage facility
The storage facility has
an area for receipt of the waste, low dose storage area and a high dose storage area.
The facility is equipped with physical protection systems that renders the stored waste materials safe and secured against intrusion, sabotage or theft.
The Centralized Waste Processing facility after the upgrade will have a
office and laboratory
operational areas for segregation of the waste materials,
Conditioning unit for disused sources
treatment of liquid waste.
National Waste Management Facilities for DSRS- Store

## Slide 7
Central Waste Processing and Storage Facility(1)

## Slide 8
Central Waste Processing and Storage Facility(2)

## Slide 9
Safety assessment and Safety Case are all in draft and have not been peer reviewed
The Safety Case covers;
  the lifecycle of the facility, from design and construction, through operation, to decommissioning
  addresses the management system, operating procedures, monitoring arrangements and emergency plans
Status of Safety Case / Safety Assessment for DSRS-Storage Facility (1)

## Slide 10
The Safety Assessment covers occupational and Public exposures;
The following principal limits have been adopted for the design and operation of the storage facility.
  design target maximum whole body dose to an individual radiation worker is 15.0 mSv/y and average of 20.0 mSv over 5 years
  design target maximum dose to the most exposed member of the public is 1.0 mSv/y
Status of Safety Case / Safety Assessment for DSRS-Storage Facility (2)

## Slide 11
Ghana has opted for the Borehole Disposal System (BDS)
A Site at the GAEC premises at Kwabenya has been chosen for the project.
National Waste Management Facilities for DSRS-Disposal Facility

## Slide 12
Drilled two exploratory boreholes ( 150m) each for detailed site characterization
Drilled Boreholes

## Slide 13
Safety Case and Safety Assessment are in draft
Both documents have undergone IAEA peer review
Concerns raised are being addressed
Status of Safety Case / Safety Assessment for The Proposed Borehole Disposal Facility (1)

## Slide 14
The Safety Assessment is for the post-closure period
  The safety Case covers all the lifecycle of the facility, from design and construction, through operation, to closure.
  it addresses the management system, operating procedures, monitoring arrangements and emergency plans as well
  There is detailed description of the disposal system.
Status of Safety Case / Safety Assessment for The Proposed Borehole Disposal Facility (2)

## Slide 15
The Safety Assessment is for the post-closure period, it covers only potential future exposures in timescales ranging from hundred to millions of years
Status of Safety Case / Safety Assessment for The Proposed Borehole Disposal Facility (3)

## Slide 16
Scenarios were identified through the Assessment Context and System Description by defining the status of external Features, Events and Processes(FEPs) for the Design Scenario
External FEPs were then reviewed and modified from the Design Scenario to identify Alternative (Defect) Scenarios
The assessment model was implemented in the AMBER software to quantify exposures.
The assessment results are used to inform stakeholder for confidence building, demonstration of safety and authorization.
Status of Safety Case / Safety Assessment for The Proposed Borehole Disposal Facility (4)

## Slide 17
Thanks for your attention