## Slide 1: Sustaining Cradle-to-Grave Control of Radioactive Sources (INT-9182) Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017
Eng. Khalil Awwad
Director of Transport & Radioactive Waste Management (DTRWM)
Nuclear Fuel Cycle Commission (NFC)
Jordan Atomic Energy commission (JAEC)
Status of Safety Cases and Safety Assessments for National Waste Management Facilities for DSRS
Hashemite Kingdom of Jordan

## Slide 2
The Nuclear Law was modified in 2007 resulting in splitting the Jordan Nuclear Energy Commission (JNEC) into two independent commissions:
  Jordan Atomic Energy Commission (JAEC)
  Jordan Nuclear Regulatory Commission (JNRC)
  JNRC in 2014 combined with another commissions to be Energy and Minerals Regulatory Commission (EMRC)
Initiating a Nuclear Power Program in Jordan
Notes: 2
2

## Slide 3: Nuclear Laws
Law No.(42) , Nuclear Energy , for the year 2007 and its amendment in 2008.
Law No.(43) , Radiation Protection and Nuclear Safety and Security for the year 2007 and its amendment in 2008.

## Slide 4: EMRC Instructions
Management of Radioactive Waste.
Management of Spent Nuclear Fuel.
Transport of Radioactive Materials.

## Slide 5: Responsibilities
  Energy and Minerals Regulatory Commission (EMRC): Regulatory body to enforce implementation of the national regulations on RWM, Inspection and issuing licensing /permits.
  Jordan Atomic Energy Commission (JAEC): Waste management organisation responsible for predisposal and disposal management of radioactive waste generated in Jordan.

## Slide 6: RWM Policy Contents
Introduction
Background
Objectives
Scope
National Radioactive Waste Management Principles
International Radioactive Waste Management Principles
Applicable National Legislation
Responsibilities
Jordan Atomic Energy Commission (JAEC)
Jordan Nuclear Regulatory Commission (JNRC)
Generators and Operators
National Centralizes RWM Facilities (NCRWMF) at JAEC
Naturally Occurring Radioactive Material (NORM)
Spent Nuclear Fuel
Decommissioning and Waste Disposal
Definition and Classification of Radioactive Waste
Implementation
References

## Slide 7
The policy allows for 3 management options for the management of DSRS:
Return of the DSRS to the supplier.
Management of the sources on the national territory.
International/regional radioactive waste management solutions.

## Slide 8: The waste management strategy for Jordan
The waste management strategy for Jordan proposes the following strategy for the safe management of DSRS
.
The strategy further allows for the generators and operators to apply delay and decay concepts for short-lived nuclides. Very importantly it instructs the establishment of a Centralized Storage facility (CSF) with sufficient capacity for treating, conditioning and storage.
In terms of disposal of DSRS the strategy mentions that planning is already underway for the establishment of a Borehole Disposal Facility therefore allowing for a waste endpoint for DSRS. Interesting to note though is the fact that the strategy document analysis the management options for the respective current and future waste types in Jordan it allows also for near-surface disposal of short lived DSRS (<30y). In such instance the condition is that it must be “retrievable emplacement into cement lined container.

## Slide 9: RWM Strategy Contents
Introduction
Objective
Scope
Strategy Statement
Management Structure for Radioactive Waste
Pre- requisites for Strategy Implementation
Radioactive Waste Generated in The Hashemite Kingdom of Jordan
Financial Provision
Predisposal Management of Radioactive Waste
Storage
Disposal of Radioactive Waste
Resources
Public Sensitivity
Uncertainties
Radioactive Waste Management Review
References

## Slide 10: Current Status
  Central storage facility at JAEC.
  Old disposal site at Sewaqa.
  RR in operation soon.
  2 JNPP with negotiation /discussion with RosAtom.

## Slide 11: Upcoming National Nuclear Facilities
  Treatment and Storage Facility for RW generated from RR.
  Near Surface Disposal Site for LILW.
  Dry Storage Facility for SNF (JNPP)

## Slide 12: Radioactive Waste in Jordan
Jordan does not yet produce any radioactive materials.
Radioactive waste in Jordan are generated from the following:
  Medicine.
  Industry
  Agriculture
  Teaching and Research centres.
  And
  Scrap and Custom Crossing Borders.
  Orphan sources.
  NORM activities.

## Slide 13: RW Stored in Jordan
This is Unsafe, Unsecured & Unacceptable

## Slide 14: RW Stored at Hospitals
This is How Radioactive Waste is Being Stored

## Slide 15: The National Centralized RW Storage Facility (CSF) at JAEC

## Slide 16: Current RW stored at the CSF

## Slide 17: National Waste Management Facilities for DSRS
Jordan has an operational national RW storage and management facility ( CSF) for DSRS at JAEC since 2010.
The CSF is equipped with all necessary tools and equipment needed for all steps of RWM
DSRS with an integrated security system.

## Slide 18: National Waste Management Facilities for DSRS
Air ventilating system
Security system.
Safe handling, conditioning of the radioactive waste, particularly the DSRS .
Safe long term interim storage of the resulting conditioned RW (waste package) for a period until a suitable repository is available for final disposal
Area of 250 m2.
Capacity of 600 drums of 200 L or 420 m3.

## Slide 19: Air Ventilation System in the CSF

## Slide 20: Liquid CSF RW Collected into a Drainage Water Tank

## Slide 21: Security System at the CSF
Security Control
Magnetic Switch
Motion Detectors
Infra Red Camera
Alarm
Key Box
Door Lock
Control Room

## Slide 22: The Radiological Emergency Response Plan for CSF
The emergency response plan for various possible radiological accidents and threatening hazards inside the CSF was prepared by JAEC and approved by JNRC.
The CSF’s emergency plan is written in Arabic.
A drills for the activation off- site emergency response plan by Jordan’s Civil Defense Forces and Public Security Forces were conducted.
Security plan for the CSF was submitted to the EMRC for approval.

## Slide 23: RWM Predisposal at CSF
The implemented procedures for the safe management of radioactive waste at the CSF as follows:
►Identification
►Assessment (when possible)
►Collection
►Transport
►Receipt
►Pretreatment
►Characterization
►Classification
►Conditioning
►Secure & Safe Storage

## Slide 24: Collection

## Slide 25: Processing

## Slide 26: Storage

## Slide 27: RWM Procedures
PR01 Process Description.
PR02 Source Acceptance
PR03 Collection-Transport.
PR04 Characterization-Dismantling.
PR05 Precemented Drums.
PR06 Conditioning DSRS-Storage.
PR07 Radiation Protection

## Slide 28: Radioactive Waste Inventory at JAEC
Total Activity | Quantity | Isotope
8420 mCi | 92 | Cs-137
145.1 mCi | 3 | Am -241
0.1 mCi | 2 | Ba -133
0.02 mCi | 13 | Co- 57
0.126 | 2 | Co -60
37450 | 1 | Co- 60
Unknown | 1 | Co - 60
1035.0 mCi | 4 | Eu - 152
0.3 mCi | 1 | Ir - 192
540.6 mCi | 8 | Ra - 226
94.3 mCi | 10 | Sr- 90
202.7 mCi | 2 | Kr- 85
3470 mCi | 11 | Am 241,Be
--- | 22 | Depleted Uranium (DU)
--- | 96 | I-131
--- | 175 | Mo99/Tc99m
--- | 2 Drum (200 L) | 14 Bag compactable Mixed Solid Waste

## Slide 29: Status of Safety Case / Safety Assessment for DSRS Stores
There is a preliminarily SC/SA for the CSF.
The first initial draft was prepared by NECSA on August 2014 .
Then updated by the CSF RWM’s Staff and reviewed by the QA Directorate at JAEC and then it is submitted to the Regulatory Authority EMRC for approval or any comments and not yet approved.
The documents are kept at the CSF ( each operator), Manager of the CSF , the QA Directorate at JAEC and ENMRC.

## Slide 30: Status of Safety Case / Safety Assessment for DSRS Stores
The scope of this daft safety case includes all the available information and identification of gaps in information required to demonstrate the safety and ensuring the safety of all radioactive waste management activities relating to DSRS as performed by the JAEC.
This will include amongst others a description of the legislation and regulations pertaining to the safe management of DSRS in Jordan, description of the regulatory functions as well as the appointed radioactive waste operator, site, facility and activity description, radioactive waste inventory, the context for the evaluation of the safety case, a safety assessment for normal and accident scenarios, a safety case compliance assessment, limiting conditions, aspects that require clarification, management systems and procedures required to ensure compliance to set safety criteria and to sustain an acceptable level of the safety.
It covered the predisposal management of the DSRS except decommissioning stage.
It includes the management system, operating procedures, monitoring arrangements and safety assessment But emergency plans are not included.

## Slide 31: Status of Safety Case / Safety Assessment for DSRS Stores

## Slide 32: Status of Safety Case / Safety Assessment for DSRS Stores
The safety assessment covers both occupational and public exposures resulting from both normal operational exposures and accidents and emergency situations.
Normal operational cover: all operations that have been performed for the dismantling and storage of all DSRS that are currently stored at CSF; all operations from their collection at the radioactive waste from the producers to their emplacement at CSF are included.
However, it was concluded that there is no exposure of the public associated with normal operations with DSRS, since there are no releases of radioactive to the environment from the CSF activities, since members of the public do not have access to the CSF.
Accidents and emergency situations cover:

## Slide 33: Status of Safety Case / Safety Assessment for DSRS Stores Normal operational covers:
Table 4: Endpoints Considered in the Assessments for Normal Operation Scenarios |  |  | 
Operator | Sv/y | Doses to an operator who is involved in all operations excluding for the transport of sources , the surveillance and inspection works. | Inside
Driver |  | Doses to a driver during the transport of DSRS from the radioactive waste generator to the CSF at JAEC. | Outside
RPO |  | Dose to the Radiation Protection Officer involved in the surveillance and inspection works. | Inside
Public |  | Doses to a representative individual from the population that receives the highest exposure from the facility. | Outside

## Slide 34: Status of Safety Case / Safety Assessment for DSRS Stores Detailed Normal operational covers
ACTIVITY | Description of activity
Driving to the site of the existed radioactive waste at user premises | Exposure of driver and operators during driving to the off-site (user’s permises) for collecting the DSRS from its generating point. The DSRS are within their original shielded container.
Dose rate measurement (off-site) | Exposure of the operators during the DSRS dose rate measurements at the off-site at its generating point/place and location. The DSRS are within their original shielded container.
Smear test (off-site) | Exposure of the operators during performing the DSRS smear test at the off-site at its generating point/place and location. The DSRS are within their original shielded container.
Identification of DSRS | Exposure of the operators during identification of the DSRS at off-site at its generating point/place and location. The DSRS are within their original shielded container.
Packaging and labeling | Exposure of the operators during Packaging and labeling for DSRS at the off-site at its generating point/place and location. The DSRS are within their original shielded container.
Loading into the truck | Exposure of the operators during loading the DSRS from the off-site into the truck. The DSRS are within their original shielded container.
Driving back to the CSF | Exposure of the operators and driver during driving form the off-site to the CSF. The DSRS are within their original shielded container.
Dose rate measurement at on – site ( CSF) | Exposure of the operators during the measurements of the dose rate of the DSRS at the site (CSF). The DSRS are within their original shielded container.
Smear test (on-site) | Exposure of the operators during performing the smear test for DSRS at the site (CSF). The DSRS are within their original shielded container.
Unloading the DSRS from the truck and transport them to the Room A | Exposure of the operators unloading the DSRS from truck to the reception room A
Smear test | Exposure of the operators during uploading the DSRS from truck to the reception room A.
Measurement dose rate | Exposure of the operators during uploading the DSRS from truck to the reception room A.
Measurement dose rate | Exposure of the operators during the characterization of the DSRS in the characterization room A
Reading data from the tag fixed on the DSRS package | Exposure of the operators during taking the information related to the DSRS in the characterization room A.
Physical characterization (Weight, dimension, …etc) | Exposure of the operators during the characterization of the DSRS in the characterization room A.
Fixing the CSF ID tag for the DSRS | Exposure of the operators during fixing the CSF ID for the DSRS in the characterization room A.
Handling 200 L Drum contained the DSRS | Exposure of the operators during the handling the DSRS drum in room A.
Close 200L Drum | Exposure of the operators during the Characterization of DSRS in the characterization room A.
Measurement of the dose rate for the drum at its surface & 1 m | Exposure of the operators during the dose rate measurements at the contact point and at (1 m) from the drum in the characterization room A.
Fixing CSF TAG for the drum | Exposure of the operators during fixing the CSF ID tag for the drum in the characterization room A.
Handling the drum by Forklift to shelf | Exposure of the operators during handling the drum inside CSF to the designated shelf in room D.
Handling the drum in Room D | Exposure of the operators during handling the 200 L drum in room D.
Drums Storage in Room D | Exposure of the operators during storing the drum on its designated shelf in room D.
Handling the radioactive source in Room W. | Exposure of the operators due to handling radioactive source in room W by the movable crane.
Storing the radioactive source in Room W. | Exposure of the operators due to storing the radioactive source in room W.

## Slide 35: Status of Safety Case / Safety Assessment for DSRS Stores
A screening out of Potential Initiating Events (PIE) was carried out using the database of PIEs included in the GSG-3 [3] and the SAFRAN Tool, where PIEs are classified into External Natural Factors, External Human Factors and Internal Operational Factors.

## Slide 36: Status of Safety Case / Safety Assessment for DSRS Stores
Table 9: Results of Screening Out of External Natural PIEs Performed with the Aim of Deriving Accidental Scenarios to be Considered in the Safety Assessment. |  | 
Name | Relevance | justification (if not relevant)
Lightning (effect on power supply) | Not relevant | There is conventional protection against lightening in both buildings. Although storms with lightening are not very common in this area
Lightning (effect on surroundings of facility) | Not relevant | There is conventional protection against lightening in both buildings. Storms with lightening are not very common in this area
Lightning (effect on facility) | Not relevant | There is conventional protection against lightening in both buildings. Although storms with lightening are not very common in this area
Extreme snowing | Relevant | 
Extreme rain | Relevant | 
Extreme drought | Relevant | 
Strong wind | Relevant | 
Sand storm | Relevant | 
Strong dust | Relevant | 
Extreme temperatures | Relevant | 
Ground instability | Relevant | 
Seismic conditions | Relevant | 

## Slide 37: Status of Safety Case / Safety Assessment for DSRS Stores
Table 10: Results of Screening Out of External Human Induced PIEs Performed with the aim of deriving Accidental Scenarios to be Considered in the Safety Assessment. For Relevant PIEs, the Linked Scenarios are Indicated. |  | 
Name (short name) | Relevance | justification SCENARIO (if not relevant)
Explosions | Not relevant | This facility is not nearby where explosions could occur.
Fire | Relevant | 
Aircraft crash and other unpredicted mobile sources. | Not relevant | The probability of aircraft crash is extremely low.
Missile due to structural or mechanical failure in nearby installations | Not relevant | No such nearby installations where failures could lead to missiles impacting the facility.
Ground subsidence or collapse due to tunneling or mining activities. | Not relevant | No such activities that could take place at the site
Ground vibration | Not relevant | No activities causing ground vibration that may occur at the site
Sabotage | Relevant | 
Theft | Relevant | 
Floods due to dam failures | Relevant | 
The release of any corrosive, toxic and/or radioactive substance | Not relevant | Installations that releases toxic substances do not exist at the site
External impacts from industrial and military installations, transport routes of hazardous material etc. | Not relevant | No such installations exist in the area, transport routes of hazardous materials do not exist in this area
Power supply and the potential loss of power | Not relevant | There is backup power supply
Civil strife and war | Relevant | 

## Slide 38
Table 11: Results of Screening out of Internal PIEs performed with the aim of deriving Accidental Scenarios to be considered in the Safety Assessment. For relevant PIEs, the linked scenarios are indicated. |  | 
Name | Relevance | justification SCENARIO
The acceptance (inadvertent or otherwise) of incoming waste, waste containers, process chemicals, conditioning agents, etc., that do not meet the specifications (acceptance criteria) included in the design basis. | Not relevant | The existing procedures both by the operator and the regulator prevent these types of events from occurring.
The processing of waste that meets acceptance criteria but that is subsequently processed in an inappropriate way for the particular type of waste; inadvertently or otherwise. | Relevant | 
A criticality event due to the inappropriate accumulation of fissile material, change of geometrical configuration, introduction of moderating material, removal of neutron absorbing material or various combinations of these. | Not relevant | Fissile materials do not exist in the facility
Explosion due to the evolution of explosive gas mixtures. | Not relevant | There are no explosive gas mixtures in the facility.
Spontaneous combustion. | Not relevant | Substances that can be subject to spontaneous combustion are not present in the facility
Local hot spots generated by malfunctions of structures, systems or components. | Not relevant | No such failures exist that can generate hot spots
Sparks from machinery, equipment or electrical circuits. | Relevant | 
Sparks from human activities such as welding or smoking. | Relevant | 
Explosions | Relevant | 
Gross incompatibilities between the components of a process system and the materials introduced into the system. | Not relevant | No such processes exist where materials are introduced into the system

## Slide 39
The degradation of process materials (chemicals, additives or binders) due to improper handling and storage. | Not relevant | No such process materials are used in the facility
The failure to take account of the non-radiological hazards presented by the radioactive waste (physical, chemical or pathogenic). | Not relevant | Non-radiological hazards are not present in the radioactive waste of type DSRS.
The generation of a toxic atmosphere by chemical reactions due to the inappropriate mixing or contact of various reagents and materials. | Not relevant | This type of events is not relevant for DSRS
Dropping radioactive waste packages or other loads due to mishandling or equipment failure, with consequences to the dropped radioactive waste package and possibly to other radioactive waste packages or to the structures, systems and components of the facility. | Relevant | 
Collisions of vehicles or suspended loads with the structures, systems and components of the facility or with radioactive waste packages, radioactive waste containment vessels and pipes. | Relevant | 
Failures of structures, systems and components | Relevant | 
The generation of missiles and flying debris due to the explosion of pressurized components or the gross failure of rotating equipment. | Not relevant | Pressurized components and rotating equipment are not present in the facility
The malfunctioning of heating or cooling equipment, leading to unintended temperature excursions in process systems or storage systems. | Not relevant | Such equipment is not present in the facility
The malfunctioning of process control equipment. | Not relevant | Such equipment is not used for DSRS
The malfunctioning of equipment that maintains the ambient conditions in the facility, such as the ventilation system or dewatering system. | Not relevant | Not relevant for operations with DSRS

## Slide 40
The malfunctioning of monitoring or alarm systems so that an adverse condition goes unnoticed. | Relevant | 
Incorrect settings (errors or unauthorized changes) on monitors, alarms or control equipment. | Relevant | 
The failure to function when called upon of emergency equipment such as the fire suppression system, pressure relief valves and ducts. | Not relevant | Such systems are not present at the facility
The failure of the power supply, either the main system or various subsystems. | Relevant | 
The malfunctioning of key equipment for handling radioactive waste, such as transfer cranes or conveyors. | Relevant | 
The malfunctioning of structures, systems and components that control releases to the environment, such as filters or valves. | Not relevant | Not relevant for operations with DSRS
The failure properly to inspect, test and maintain structures, systems and components. | Relevant | 
Incorrect operator action due to inaccurate or incomplete information. | Relevant | 
Incorrect operator action in spite of having accurate and complete information. | Relevant | 
Sabotage by employees. | Relevant | 
The failure of systems and components such as incinerator linings, compactor hydraulics or cutting machinery that poses the risk of significant additional radiation exposure of personnel called on to assist in effecting repairs or replacements. | Not relevant | Such systems are not used in the operation with DRSS
Encountering an unanticipated radiation source in decommissioning (e.g. different in nature or amount) and not recognizing immediately the changed circumstances. | Not relevant | Decommissioning is outside the scope of this safety assessment
Removing or weakening a structure or component in decommissioning without realizing the possible effect on the structural competence of other structures and components. | Not relevant | Decommissioning is outside the scope of this safety assessment
Traffic accident when transporting radioactive waste on-site to processing facility or from processing facility to storage building | Not relevant | The storage and processing facility are very close to each other and there is no transport between them

## Slide 41: Doses Resulted from Normal Operation Scenarios
Table 13: Calculated values of the annual doses for the different assessment normal operation scenarios. |  |  | 
Impact | Endpoint | Dose (Sv/year) | Limit (Sv/y)
Driving to the radioactive waste site | Dose to worker | 2.00E-006 | 2.00E-002
Dose rate measurement (off-site) | Dose to worker | 1.20E-007 | 2.00E-002
Smear test (off-site) | Dose to worker | 6.00E-008 | 2.00E-002
Identification of DSRS | Dose to worker | 4.80E-007 | 2.00E-002
Packaging and labeling | Dose to worker | 8.00E-006 | 2.00E-002
Loading to the truck | Dose to worker | 8.00E-006 | 2.00E-002
Driving back to CSF | Dose to worker | 1.00E-004 | 2.00E-002
Dose rate measurement (on-site) | Dose to worker | 2.40E-007 | 2.00E-002
Smear test (on-site) | Dose to worker | 6.00E-008 | 2.00E-002
Downloading from truck and transport to Room A | Dose to worker | 4.00E-006 | 2.00E-002
Smear test | Dose to worker | 6.00E-008 | 2.00E-002
Measurement Dose Rate | Dose to worker | 1.20E-007 | 2.00E-002
Measurement Dose rate | Dose to worker | 1.20E-007 | 2.00E-002
Take data from tag | Dose to worker | 4.80E-007 | 2.00E-002
Physical characterization (weight, dimension ...etc.) | Dose to worker | 3.00E-006 | 2.00E-002
Put CSF tag | Dose to worker | 1.00E-006 | 2.00E-002
Handling to 200 L Drum | Dose to worker | 9.00E-006 | 2.00E-002
Close 200L Drum | Dose to worker | 1.00E-006 | 2.00E-002
Measurement Dose rate for drum at surface & 1 m | Dose to worker | 5.00E-007 | 2.00E-002
Put CSF TAG for drum | Dose to worker | 5.00E-007 | 2.00E-002
Handling the drum by Forklift to shelf | Dose to worker | 5.00E-006 | 2.00E-002
Compaction for medical waste (tubes. gloves, ...etc.) | Dose to worker | 5.00E-007 | 2.00E-002
Source handling in Room W | Dose to worker | 4.50E-006 | 2.00E-002
Source storage in Room W | Dose to worker | 7.50E-006 | 2.00E-002
Total | Dose to worker | 1.56E-004 | 2.00E-002
Doses estimated for all scenarios are below the Reference Level of 1 mSv. |  |  | 

## Slide 42: Analysis for Accident scenarios
Table 14: Accident scenarios that have potential radiological impacts inside the facility. |  |  |  |  | 
Scenario | Impact | Probability - qualitative | Endpoint | Case | Dose (Sv)
Damage of source during handling into the 200L drum | Impact for scenario Damage of source during handlinginto 200L drum | Low | Worker inside the CF | Assessment case | 8.98E-016
Dropping waste packages during handling Drum into the shelf | Impact for scenario Dropping waste packages during handling Druminto the shelf | Low | Public |  | 3.21E-020
Dropping source through handling by crane in Room W | Impact for scenario Dropping source through handling by crane in Room W | Low | Worker inside the CF e |  | 6.40E-010
Fire | Impact for scenario Fire | Very Low | Public |  | 1.28E-009
Doses estimated for all scenarios are much lower than the Reference Level of 1 mSv. |  |  |  |  | 

## Slide 43: Accident Scenarios
Table 15: Accident scenarios that have potential radiological impacts outside the facility. |  |  |  |  | 
Scenario | Impact | Probability - qualitative | Endpoint | Case | Dose (Sv)
Car crush | Impact for scenario Car crush | Medium | Worker outside | Assessment case | 3.00E-016
Car crush | Impact for scenario Car crush | Low | Worker outside |  | 6.41E-017
Damage of waste package through Loading into the truck | Impact for scenario Damage of waste package through Loading to the truck | Low | Worker outside |  | 5.99E-016
Damage of waste package through Loadinginto the truck | Impact for scenario Damage of waste package through Loading to the truck | Low | Worker outside |  | 1.28E-016
Doses estimated for all scenarios are much lower than the Reference Level of 1 mSv. |  |  |  |  | 

## Slide 44: Status of Safety Case / Safety Assessment for DSRS Stores
All calculations related to the dose assessment from various activities of the CSF at JAEC were performed in this safety assessment using the methods and models described in the SADRAMS methodology, and using the SAFRAN dose assessment Tool, which implements these methodologies and modeling.
Calculation of doses from external irradiation
All doses from external irradiation were calculated by multiplying the measured or calculated dose rates by the exposure time, in hours/year for impacts of normal operation scenarios or in hours for impacts of accidental scenarios. The dose rates were calculated from the activity of the sources involved in the scenario and taking into account the reduction of the dose rates by shielding. The calculations were performed by using the models available in the SAFRAN Tool for the calculation of doses from a point source with (lead) shielding and without shielding
The assessment results used to manage and optimized the radiation worker doses .

## Slide 45: Sewaqa Disposal Site

## Slide 46: Old Disposal Site at Sewaqa
The main gate to the RW disposal site
Site At Sewaqa
The RW Disposal Site at Sewaqa
RW Disposal Pit at Sewaqa
Partially Constructed processing facility

## Slide 47: Disposal Site at Sewaqa
The RW Disposal Site at Sewaqa
Underground disposal site
Reinforced concrete underground pit , dimension 3.6 m x3.6 m with depth 3.1 m.
Backfilling with good compacted natural materials (gravel, clay, concrete ) with drainage pipe surrounded with sand
Consists of three layers , each layer accommodates 25 drums 200 L.
Spent sealed sources in its cask and container are conditioned in cement mortar .
A heavy lid needs a special crane .

## Slide 48: Old Disposal Site at Sewaqa

## Slide 49: Radioactive Waste in Sewaqa (Disposal RW Site)
Radionuclides | No. of Sources | Total Activity (mCi) / Year | Comments | Applications
Cs-137 | 33 | 3500(2007) 15 (Unknown) | Conditioned in 25 steel drums of 200 L | Industrial Nuclear Gauges
Co-60 | 43 | 3500 (2007) | Conditioned in three steel drums of 200 L | Industrial Nuclear Gauges
Sr-90 | 6 | 50 (2007) | Conditioned in one steel drum of 200 L | Industrial Nuclear Gauges
Cs-137 Tubes | 30 | 560 (1999) | Conditioned in one steel drum of 200 L | Medical Bracyhtherapy
Cs-137 Needles | 54 | 100 (1999) |  | Medical Brachytherapy
Am-241 | 5 | 225 | Conditioned in two steel drums of 200 L | Industrial Nuclear Gauges
No. of radioactive sources = (171) |  |  | No. of drums = (32) | 

## Slide 50: NORM Disposal at Sewaqa

## Slide 51: Status of SC/SA for DSRS Disposal Facilities
NO, SC/SA for Sewaqa old disposal site.

## Slide 52
Thank You