## Slide 1: Sustaining Cradle-to-Grave Control of Radioactive Sources (INT-9182) Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017
-EL ABBARI Younes, FADIL Najib
(CNESTEN)
-SADIQ Younes
(AMSSNuR)
Status of Safety Cases and Safety Assessments for Moroccan Long Term Storage Facility

## Slide 2: National Waste Management Facilities for DSRS
  The legislation in Morocco (law n° 17-83) determines that the responsibility for the management of radioactive waste is carried by the National Centre of Nuclear Energy, Sciences and Techniques (CNESTEN).
  Centralized waste management facilities was established by CNESTEN and licensed by regulatory body base on the safety analysis report.
  CENM is located 22 km north of Rabat-Salé, 8 km to the east of the Atlantic coast and it covers an area of 24.75 hectares.
  Description of the facility:

## Slide 3: National Waste Management Facilities for DSRS
  Description of the facility:
Long term storage facility: it consists of four vaults with a surface area of 52 m2 for each one ,a height of 3.5 m, and a capacity of 616 drums/vault. The thickness of the concrete walls is 0.40 m.

## Slide 4: National Waste Management Facilities for DSRS
The application for authorization of Nuclear Facilities and Nuclear Activities, as well as Final Disposal Facilities, the content of which is laid down by regulation, must include facility safety analysis report including a site selection evaluation report and an environmental impact assessment of the Installation, an internal emergency plan and a physical protection plan, updated in the different phases of authorization.

## Slide 5: National Waste Management Facilities for DSRS
For the existing store facility , there is a Final Safety Case
  The SC document was reviewed by a safety commission constituted by representatives from the ministry of health, the ministry of Interior, the ministry of Energy and Mine and the Environment Department
  It Has been formally approved, Therefore we have our operation licence
  A copy of this document is kept by the operator (CNESTEN) and a copy kept by RB

## Slide 6: National Waste Management Facilities for DSRS
Draft document to apply for authorisation for modification of the conditioning of DSRS in working shields to the dismantlement of DSRS, and to demonstrate the safety of dismantlement, conditioning and storage of Category 3 to 5 DSRS as well as to determine any actions necessary for the improvement of safety.

## Slide 7: National Waste Management Facilities for DSRS
Decree No.2-94-666 concerning the authorizations and control of nuclear installations states that the following steps in the lifecycle of nuclear installations are subject to authorization:
Construction
Discharges of radioactive liquid and gaseous effluents
Commissioning
Operation
Decommissioning
Scope and contents of the SC/SA for the store(s)

## Slide 8: National Waste Management Facilities for DSRS
The Article 7 (decree No.2-94-666) related to the construction authorization in this decree states that: Construction authorization application must be accompanied by a preliminary safety analysis report. This report includes the following chapters:
General description of the site
Geography
Risk assessment due to air traffic
Demography
Meteorology
Descriptive geology and geotechnical
Dynamic Geology and Seismicity
Hydrology
Hydrogeology
Radiological baseline
1/5-Construction authorization
Scope and contents of the SC/SA for the store(s)

## Slide 9: National Waste Management Facilities for DSRS
2/5-Authorization of discharges of liquid and gaseous radioactive effluents
Scope and contents of the SC/SA for the store(s)
Article 9 (decree No.2-94-666): The application for authorization of discharges of liquid and gaseous radioactive effluents must be accompanied by a document giving information about systems intended for the treatment of liquid and gaseous effluents to maintain the amount and concentration of the discharged effluents into prescribed limits.

## Slide 10: National Waste Management Facilities for DSRS
Article 12 decree (No.2-94-666): The application for Commissioning tests authorization must be accompanied by a provisional safety analysis report. This report contains , notably:
The design of the nuclear facility and Its operating procedures;
Analysis of postulated accidents and the ability of safety systems to limit the consequences.
3/5-Commissioning authorization
Scope and contents of the SC/SA for the store(s)

## Slide 11: National Waste Management Facilities for DSRS
The application for authorization of operation must be accompanied by the definitive safety report which shall include in particular:
1-The results of commissioning tests.
2-The operational programs and the detailed procedures for operating the installation, including:
normal operation ;
incidents and accidents expected.
4/5-Operation authorization
Scope and contents of the SC/SA for the store(s)

## Slide 12
  The safety assessment covers both Occupational exposures and Public exposures
  Normal operational exposures: regarding the storage facility it covers all the operation performed inside this facility: Storing the final packages of radioactive waste, surveillance operations, maintenance operations....
  Accidents and emergency situations: Fire in a vault full of RW packages (drums), Dropping a waste package ...
National Waste Management Facilities for DSRS

## Slide 13: Status of Safety Case / Safety Assessment for DSRS Stores
  The exposure scenarios were identified and described Based on the operational programs and the adopted procedures for operating the installation
  Exposures were quantified Using the hot spot-software
  The assessment results are used:
    to manage/optimise worker doses
    to define monitoring plans

## Slide 14: Thank you!
Notes: Thank you!