## Slide 1: Sustaining Cradle-to-Grave Control of Radioactive Sources (INT-9182) Meeting on the development, revision and implementation of the safety case and safety assessment Indonesia, 15 – 19 May 2017
Edmundo P. Vargas – Philippine Nuclear Research Institute (PNRi)
Alfonso A. Singayan –Philippine Nuclear Research Institute (PNRi)
Rose E. Quicho – AMH Philippines, Inc. (TSO)
Editha A. Marcelo – Philippine Nuclear Research Institute (PNRi)
Philippine Nuclear Research Institute
Commonwealth Avenue
Quezon City , Philippines
Status of Safety Cases and Safety Assessments for National Waste Management Facilities for DSRS
Philippines

## Slide 2: Dual Role of Promotion and Regulation
The PNRI center of nuclear science and technology activities in the Philippines.
It is one of the research institutes under the Department of Science and Technology.

## Slide 3: National Waste Management Facilities for DSRS
Near Surface and Borehole Disposal Facility (Proposed)
Gattaran, Cagayan
Near Surface Interim Storage Facility (Existing)
Commonwealth, Quezon City

## Slide 4: National Waste Management Facilities for DSRS
Commonwealth Avenue
Near Surface Interim Disposal Facility
Interim Storage Facility
  Intended to manage short-lived radionuclide (λ<30 yrs) and temporarily contain radioactive wastes with longer half life.
  Located within the Philippines Nuclear Research Institute (PNRI) compound in Commonwealth, Quezon City. Trenches A, B, C
  Constructed In 1980
Quezon Memorial Circle

## Slide 5: National Waste Management Facilities for DSRS

## Slide 6: PNRI Radwaste Interim Storage and Treatment Facilities
300 x 200-L drum capacity
Trench A
5m W x 3.5m H x18m L
Trench B
3.5m W x 3.5m H x 18m L
A
B
C
A
B
C

## Slide 7: PNRI Radwaste Interim Storage and Treatment Facilities
Unconditioned Waste Trench C
Trench A
Trench B

## Slide 8: Generators of Disused Sources (1/3)
Medical Applications (teletherapy sources)
Medical Applications (teletherapy sources)

## Slide 9: Generators of Disused Sources (2/3)
Research & education application (irradiator sources)

## Slide 10: Generators of Disused Sources (3/3)
Industrial application (nuclear gauges)

## Slide 11: Options for Disposal of Disused Sources
Return to original supplier/ manufacturer
Transfer to an authorized person
Disposal to an authorized person and facility

## Slide 12: Management of Disused Sources
Drum Storage of Disused Sources

## Slide 13: Conditioned Disused Sealed Sources
Available in 87 by 200-L drums with total activity 1.68E+11 Bq after 300 years

## Slide 14: Conditioned Teletherapy sources
Contained in 9 stainless steel containers (1 m3 volume)
Total Activity of 0.002 Bq after 300 years

## Slide 15: Safety on Conditioning of Ra-226 Sources
560 mg Ra-226 sources were encapsulated in 10 stainless steel vials & emplaced in the lead shield container with external dose rate of 1.2 mSv/hr

## Slide 16: Conditioning of SHARS by NECSA Through the Initiative of the IAEA
Mobile Hot Cell
Teletherapy Sources
18 units of teletherapy
sources
4 units irradiator sources

## Slide 17: Long Term Storage Shield

## Slide 18: Sources Conditioned/Unconditioned
Conditioned
13 units teletherapy sources (1.95E+14) Bq
3 units irradiator sources (8.61E+12)Bq
Unconditioned
5 units teletherapy sources (~7.2E+13)Bq
1 unit irradiator source (~1.14E+12)Bq

## Slide 19: Status of Safety Case / Safety Assessment for DSRS Stores
Interim Storage Facility
  Status of Safety Case / Safety Assessment
  *Reviewed by regulator every year
 | Yes | No | Remarks
Final | ✓* |  | 
Peer Review | ✓ |  | By IAEA
Reviewed by Operator | ✓ |  | By RPS-NSD PNRI
Reviewed by Regulator | ✓ |  | By NRD PNRI
Formally Approved | ✓ |  | By PNRI
Documentation | ✓ |  | By RP-NSD PNRI

## Slide 20: Status of Safety Case / Safety Assessment for DSRS Stores
Interim Storage Facility
  Scope of Safety Case / Safety Assessment
 |  | Covered? | 
 |  | Yes | No
Lifecycle of Facility | Design and Construction |  | ✓
 | Operation | ✓ | 
 | Decommissioning |  | ✓
Administrative Guide | Management System | ✓ | 
 | Operating Procedure | ✓ | 
 | Monitoring Arrangements | ✓ | 
 | Emergency Plans | ✓ | 
 | Safety Assessment | ✓ | 

## Slide 21: Status of Safety Case / Safety Assessment for DSRS Stores
Interim Storage Facility
  Exposure Level
 |  | Exposure (mSv/yr)
Occupational |  | 50
Public |  | 1
Normal Operational | *Processing of Radwaste | 2
Emergency Situation | Direct Exposure to DSRS due to human error | 0.105 mSv/yr
 | *Fire | 
 | *Spill of Liquid Waste | 46 µSv/yr

## Slide 22: National Waste Management Facilities for DSRS
Co-located Near Surface and Borehole Disposal Facility
  Intended to manage both short and long-lived radionuclides.
  Proposed Location: Gattaran, Cagayan Valley.
Cagayan River
Collocated Near surface and Borehole Disposal Site
Cagayan North International Airport
Facility Footprint
Mt. Bantay Kalbo

## Slide 23: National Waste Management Facilities for DSRS
Co-located Near Surface and Borehole Disposal Facility
  Conceptual Stage
    Detailed Engineering
Near Surface Vaults / Repository

## Slide 24: Investigations Conducted
Site selection
Preliminary Environmental Baseline Characterization including demographic studies
Geological and hydrogeological studies
  Geological and hydrogeological studies
  Water Balance
  Drilling investigation
    Geotechnical studies
    Permeability studies (packer tests and in-situ soil permeability tests
BDC Scoping Calculations
Hydrological Modelling using Hydrus 1
Amber Modelling (Preliminary and assisted by Quintessa

## Slide 25: Location of Investigation Boreholes

## Slide 26: Investigations

## Slide 27: Current Geological Model

## Slide 28: Investigation Results
No monolithic block
Rock formation
  Oligocene layered volcanic pyroclastics
  Highly fractured
  Water table aquifer at depth of 70m below ground surface reckoned from the hilltop
  Permeability
    Soil /Weathered Rock 0-5m– 15 m/d
    Weathered and fractured rock, 5m – 70m 0.2 m/d
    Slightly weathered and fractured > 70m – 0.02 m/d
Preliminary BDC Scoping calculations
  Problem with Am and Ra sources
Preliminary Erosion Studies
  Average Erosion Rate in Region II, Cagayan, Philippines (Based on Department of Agriculture Studies)
  As secondary forest – 3.0 tons/ha/year
  Average of 0.7 cm per year or around 70 cm/ 100 years
  Exposure of Borehole due to erosion (no modelling)
  7 meters for 1000 years (assuming constant rate of erosion)
Looking at Disposal Zone between 100 to 200 m depth below ground surface
  Within the saturated zone
50 capsules for disposal based on present inventory (2500 sources)

## Slide 29: Status of SC/SA for DSRS Disposal Facilities
Co-located Near Surface and Borehole Disposal Facility
  Status of Safety Case / Safety Assessment
 | Yes | No | Remarks
Final |  | ✓ | Iteration 1
Peer Review | ✓* |  | By IAEA
Reviewed by Operator | ✓* |  | By SDS-NRD PNRI
Reviewed by Regulator |  | ✓* | By NRD PNRI
Formally Approved |  | ✓ | By PNRI
Documentation | ✓ |  | By PNRI

## Slide 30: Status of SC/SA for DSRS Disposal Facilities
Co-located Borehole Disposal Facility
  Status of Safety Case / Safety Assessment
 |  | Covered? | 
 |  | Yes | No
Lifecycle of Facility | Design and Construction | ✓ | 
 | Operation | ✓ | 
 | Decommissioning | ✓ | 
Administrative Guide | Management System | ✓ | 
 | Operating Procedure | ✓ | 
 | Monitoring Arrangements | ✓ | 
 | Emergency Plans | ✓ | 
 | Safety Assessment | ✓ | 

## Slide 31: Status of SC/SA for DSRS Disposal Facilities
Borehole Disposal Facility
  Scenarios Analysis:
    Defect Scenario
      it is assumed that not all components of the near field perform as envisaged in the Design Scenario due to either defective manufacturing of waste packages (e.g. welding defects), or defective implementation in the borehole (e.g. improper emplacement of cement grout).
    Unexpected Geological Characteristics Scenario
      it is assumed that the actual performance of the geosphere from a safety perspective is worse than the expected performance.
    Changing Environmental Conditions Scenario
      it is assumed that the disposal system is affected by climate change resulting in modifications to certain geosphere characteristics (e.g. groundwater recharge rates) and biosphere characteristics (e.g. water demand, surface erosion rates).
    Borehole Disturbance Scenario
      it is assumed that drilling of a water abstraction borehole immediately adjacent to the disposal borehole results in the disturbance of the disposal borehole and the earlier release of radionuclides from the near field and subsequent exposure of humans to radionuclides (e.g. due to the use of contaminated water from the abstraction borehole).

## Slide 32: Status of SC/SA for DSRS Disposal Facilities
Borehole Disposal Facility
  Timeframes for the Various Activities:
Activity | Timeframe
Borehole Construction and Waste Emplacement | One year
Site Closure | Immediately following the waste disposal operation
Institutional Control Period (e.g. surveillance, local/national government records, planning authority restrictions, site marked on official maps) | 50 years*
No control (neither active nor passive) – all records/knowledge conservatively assumed to be lost | From 50 years onwards
*From Sensitivity Analysis 30-100 years

## Slide 33: Current Activities for BDS
Monitoring of Boreholes and Site
Set-up Meteorological Station
Refine Geological/Hydrogeological Model
Survey and development of Access Road
Soil Erosion studies
Preparation and review of 1st iteration of the Post Closure Safety Assessment
Challenges
Social Acceptability issues
Inadequate funds

## Slide 34: Thank you!
Notes: Thank you!